## Slide 1
Export of Segment Routing IPv6 Information in IPFIX draft-ietf-opsawg-ipfix-srv6-srh-02
Enabling insights in SRv6 forwarding plane
by adding Segment Routing dimensions
thomas.graf@swisscom.com
benoit.claise@huawei.com
pierre.francois@insa-lyon.fr
22. October 2022

## Slide 2: SRv6 @ IPFIX Draft Status
Received comments from SPRING, OPSAWG and network vendors working on implementations and
Addressed all open issues. Verified with IANA how to manage the srhFlagsIPv6 and srhSegmentEndpointBehavior registries. Outcome is to have a reference to the "Segment Routing Header" registry instead of listing the entries in the IPFIX registry.
Expanded the terminology section to have a consolidated view on which terms are inherited from which RFC.
Added "Segment Routing Policy" in the srhActiveSegmentIPv6Type registry.
Added "Multiple Segment Routing Headers" in the "Operational Considerations" section.
Corrected "Template Record and Data Set with SRH Section" example.

## Slide 3: SRv6 @ IPFIX VPP implementation status – lab topology
Describe lab topology.
Describe where source code is available. Current limitations and next steps.

## Slide 4: SRv6 @ IPFIX VPP implementation status – record order matters
Shows an IPFIX data-template example for a IPv6 encapsulated SRv6 Packet. IPFIX entity sourceIPv6Address appears twice.
Order of the data records matter as described in Section 8 of [RFC7011]. Distinguishes between the tunneled Customer Data Plane and the Provider Data Plane.
1
2
7

## Slide 5: SRv6 @ IPFIX VPP implementation status – records exposed
srhActiveSegmentIPv6
  128-bit IPv6 address that represents the active SRv6 segment.
srhSegmentEndpointBehavior
  16-bit unsigned integer that represents a SRv6 Endpoint behavior as per Section 4 of [RFC8986].
srhSegmentIPv6sLeft
  8-bit unsigned integer defining the number of route segments remaining to reach the end of the segment list.
srhFlagsIPv6
  8-bit flags defined in the SRH.
srhTagIPv6
  16-bit tag field defined in the SRH that marks a packet as part of a class or group of packets sharing the same set of properties.
srhSegmentIPv6ListSection
  Exposes the SRH Segment List as defined in section 2 of [RFC8754] as series of n octets.
srhSegmentIPv6BasicList
  Ordered basicList [RFC6313] of zero or more 128-bit IPv6 addresses in the SRH that represents the SRv6 segment list. The Segment List is encoded starting from the active segment of the SR Policy.
1
2
3
4
5
6
7

## Slide 6: SRv6 @ IPFIX Huawei VRP implementation status – lab topology
Describe lab topology.
Describe where source code is available. Current limitations and next steps.

## Slide 7: SRv6 @ IPFIX Huawei VRP implementation status – records exposed
srhActiveSegmentIPv6
  128-bit IPv6 address that represents the active SRv6 segment.
srhSegmentIPv6sLeft
  8-bit unsigned integer defining the number of route segments remaining to reach the end of the segment list.
srhFlagsIPv6
  8-bit flags defined in the SRH.
srhTagIPv6
  16-bit tag field defined in the SRH that marks a packet as part of a class or group of packets sharing the same set of properties.
srhSegmentIPv6ListSection
  Exposes the SRH Segment List as defined in section 2 of [RFC8754] as series of n octets.
According to A.1.2. Template Record and Data Set with Segment List Section
1
2
3
4
5
6
7

## Slide 8: SRv6 @ IPFIX Huawei VRP implementation status – options exposed
srhSegmentIPv6
  128-bit IPv6 address that represents a SRv6 segment.
srhSegmentLocatorLength
  8-bit The number of significant bits. Together with srhSegmentIPv6 it enables the calculation of the SRv6 Locator.
srhSegmentEndpointBehavior
  16-bit unsigned integer that represents a SRv6 Endpoint behavior as per Section 4 of [RFC8986].
According to A.2. Options Template Record and Data Set for SRv6 Segment End Point behavior and Locator Length
1
2
3
4
5
6
7

## Slide 9: SRv6 @ IPFIX Next Steps
Missing SRv6 data-plane visibility is a recognized problem.
Open-source running code published.
First commercial vendor implementations will be public end of Q1 and Q3 2023.
The authors would like to ask the OPSAWG working group wherever it beliefs that the document is in stable state to request early code point allocation at IANA or not.
thomas.graf@swisscom.com
benoit.claise@huawei.com
pierre.francois@insa-lyon.fr
22. October 2022