## Slide 1
Export of Segment Routing IPv6 Information in IPFIX draft-tgraf-opsawg-ipfix-srv6-srh
Enabling insights in SRv6 forwarding plane
by adding Segment Routing dimensions
thomas.graf@swisscom.com
benoit.claise@huawei.com
12. March 2022

## Slide 2: MPLS-SR @ IPFIX Adressed with RFC 9160 @ OPSAWG
In MPLS-SR the data-plane is still the same as in MPLS. Only the routing protocol providing the label changes.
IE70 mplsTopLabelStackSection is the top label FEC used to forward. Each following label in the label stack is decomposed in IE71-79 separately.
  0 1 2
  0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  | Label | Exp |S|
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  Label: Label Value, 20 bits
  Exp: Experimental Use, 3 bits
  S: Bottom of Stack, 1 bit
IE47 mplsTopLabelIPv4Address is the top label IP address where the traffic is forwarded to.
IE46 mplsTopLabelType describes from which routing protocol the top label IP address and label is coming from. Updated with RFC 9160 to cover MPLS-SR routing protocols.

## Slide 3: SRv6 @ IPFIX Adressed with draft-tgraf-opsawg-ipfix-srv6-srh
SRv6 is already deployed at network operators (draft-matsushima-spring-srv6-deployment-status). Unaware of any network operator migrated from MPLS to SRv6 yet.
  -> Feedback welcome
Data-Plane visibility is missing in SRv6. Unable to see how much traffic is being forwarded or dropped with which SID. Network operators flying blind.
Segment Routing Header is defined in Section 2 of RFC 8754.
Segment List doesn't change with draft-ietf-spring-srv6-srh-compression. It is still IPv6 addressed. Context to routing protocol however is important to understand decomposition.

## Slide 4: SRv6 @ IPFIX Adressed with draft-tgraf-opsawg-ipfix-srv6-srh
ipv6SRHSegmentsLeft
  8-bit unsigned integer defining the number of route segments remaining to reach the end of the segment list.
ipv6SRHTag
  16-bit tag field defined in the SRH that marks a packet as part of a class or group of packets sharing the same set of properties.
ipv6SRHFlags
  8-bit flags defined in the SRH.
ipv6SRHSegment
  128-bit IPv6 address that represents an SRv6 segment.
ipv6SRHSegmentBasicList
  Ordered basicList [RFC6313] of zero or more 128-bit IPv6 addresses in the SRH that represents the SRv6 segment list. The Segment List is encoded starting from the active segment of the SR Policy.

## Slide 5: SRv6 @ IPFIX Adressed with draft-tgraf-opsawg-ipfix-srv6-srh
  ipv6SRHSection
  Exposes the SRH and its TLV's as defined in section 2 of [RFC8754] as series of n octets.
ipv6SRHSegmentListSection
  Exposes the SRH Segment List as defined in section 2 of [RFC8754] as series of n octets.
ipv6SRHSegmentType
  Name of the routing protocol or PCEP extension from where the active SRv6 segment has been learned from.

## Slide 6: SRv6 @ IPFIX Draft Status
Feedback collected from SPRING, OPSAWG and IPFIX doctor.
ipv6SRHSection and ipv6SRHSegmentListSection added to allow export of entire SRH and Segment List in one IPFIX entity.
ipv6SRHSegmentsLeft added to express at which position of the Segment List the forwarding happens.
Added operational considerations section to describe when ipv6SRHSection and ipv6SRHSegmentListSection makes sense.
Updated IANA considerations to be in line with RFC 8126.
The document doesn't introduce any new protocols. It is for documentation purposes. However, because new IPFIX registries are introduced, it is required to be an Internet standard document.
Authors believe that document should progress quickly through IETF to avoid private enterprise code points being used in SRv6 deployments.
-> Call for adoption at OPSAWG at IETF 113
thomas.graf@swisscom.com
benoit.claise@huawei.com
12. March 2022